## Slide 1: JPEG Image Compression
By –
Bbiswabasu Roy – 19EC39007
Jothi Prakash – 19EC39023

## Slide 2
JPEG Pipeline

## Slide 3: RGB TO YCbCr
1

## Slide 4: Color Specification Process
The YUV colour coordinate defines Y, Cb, and Cr components of one color image, where Y is commonly called the luminance and Cb, Cr are commonly called the chrominance. Describing of a colour in terms of its luminance and chrominance content separately enable more efficient processing and transmission of colour signals in many applications.

## Slide 5: Block Based DCT
2

## Slide 6: Discrete Cosine Transform Process
After colour coordinate conversion, the next step is to divide the three colour components of the image into many 8×8 blocks. For an 8-bit image, in the original block each element falls in the range [0,255]. Data range that is centred around zero is produced after subtracting The mid-point of the range (the value 128) from each element in the original block, so that the modified range is shifted from[0,255] to [-128,127]. Images are separated into parts of different frequencies by the DCT

## Slide 7: Quantization
3

## Slide 8: Quantization Process
We actually throw away data through the Quantization step. We obtain the Quantization by dividing transformed image DCT matrix by the quantization matrix used . Values of the resultant matrix are then rounded off

## Slide 9: Zig Zag Ordering
4

## Slide 10: Zig Zag Ordering Process
After quantization, the "zig-zag" sequence orders all of the quantized coefficients. In the "zig-zag" sequence, firstly it encodes the coefficients with lower frequencies (typically with higher values) and then the higher frequencies (typically zero or almost zero).

## Slide 11: Huffman Encoding
5

## Slide 12: Huffman Coding Process
Entropy Coding achieves more lossless compression by encoding more compactly the quantized DCT coefficients. Huffman coding is used in the baseline sequential codec, but all modes of operation use Huffman coding and arithmetic coding.

## Slide 13: Results
Output Images are generated by using the JPEG Image compression algorithm

## Slide 14: Cameraman
1

## Slide 15
Compression Ratio – 5.244
Compression Ratio – 7.93

## Slide 16
Compression Ratio – 11.89
Compression Ratio – 28.96

## Slide 17: Lena
2

## Slide 18
Compression Ratio – 3.87
Compression Ratio – 13.38

## Slide 19
Compression Ratio – 18.04
Compression Ratio – 30.26

## Slide 20: Corn
3

## Slide 21
Compression Ratio – 2.84
Compression Ratio – 4.55

## Slide 22
Compression Ratio – 7.18
Compression Ratio – 20.09

## Slide 23: Thank You